VESSEL NAME Implementation date Review date REFUELLING SAFETY CHECKLIST

Refuelling Preparation

Bring the vessel alongside of the refuelling facility and secure the vessel. Ensure that the distance between the fuel facility and the dock filling point is the shortest possible and place Caution sign over fuel line. Place no smoking signs on the ship and on the wharf in the vicinity of the ship and fuel facility. (Hoist flag B for refuelling in port areas where it is required). Prior to filling, ensure that all engines have been turned off and there are no signs of leaks from the tanks or fuel lines. No naked flames and no motors running. Turn off batteries. Have fire extinguishers (suitable for oil fires) available near the filling station and rags/container to catch spill as the fuel supply line is disconnected. Determine the tank ullage and fuel requirements. Check communication equipment is operational .

Refuelling

Keep the fuel nozzle in contact with the filler pipe to prevent static electricity build up. Crew member to be in Engine Room to constantly monitor the tank being filled. Constantly monitor the fuel level in the tank/s to ensure they are not over-filled. Consider stability when filling the side tanks. Fill slowly towards the end. Seal fuel tanks immediately after the fuel line has been disconnected. Ventilate for some time before starting engine.

In the event of a spillage

Stop filling Block off deck scuppers and freeing ports to contain any spill on deck. Take action to stop any further fuel from entering the water. Inform the relevant Port Authority and carry out their instructions. Advise vessels moored nearby of the spillage (pending the arrival of Port Authority). Clean up on board the vessel. Complete the pollution report documentation

Approving officer Signed Date