| VESSEL NAME Implementation date Review date RIGGING FAILURE SAFETY CHECKLIST |
| --- |
| Yes | Tack to relieve strain on shrouds, ease sheets, slow down, shorten sail, heave to or anchor - hoist NUC signals. |
| Yes | Investigate the extent of rigging failure and assess success with a jury repair or cut away broken mast. |
| Yes | Check chain plates, deck at mast step, bilge levels for possible hull damage. If damage found, water is coming in or fire is present then activate founder, excessive list, abandon ship or fire emergency procedure. |
| Yes | If failure is minor, continue with care to wharf and discharge passengers as safely as possible. |
| Yes | If failure is major, anchor vessel and call for assistance to remove passengers. |
| Yes | Complete report in vessel record book. |
| Approving officer Signed Date |