VESSEL NAME Implementation date Review date SLIPPING SAFETY CHECKLIST

Precautions before slipping Ensure repair list is prepared, conditions are fortuitous & the surveyor has the required access. Precautions at slipping Ensure structural support The entire weight of the vessel will be supported at a few localised points, instead of uniformly over the hull, as is the case when the vessel is afloat. External keel coolers, echo sounders, log and sonar transducers could be severely damaged if the bilge or keel supports came into contact with them. It is important that the dockmaster is supplied with up to date and accurate information regarding their location. Ensure stability Tanks should preferably be empty so as to remove any free surface effect. The critical moment occurs just before the vessel settles on the keel blocks. Trim vessel slightly by the stern. As the water level falls, the keel will touch the blocks at the stern first. This results in an upthrust on the stern which increases as the water level falls. This has the effect of reducing your vessel's GM by causing an apparent rise in the centre of gravity. If it did not have sufficient initial stability, it could topple off the blocks, with disastrous consequences. All moveable weights should be secured, and all unnecessary weights on deck should be removed. Precautions on slip Transducers and anodes should be covered with grease and then masking tape. Remove drain (docking) plugs from all tanks that need to be drained. Keep them safe and record which plug goes where. Ensure that plugs are all replaced prior to entry into the water. Ensure that: safe access is provided to and from the vessel. fire safety precautions are adhered to. all tanks, spaces are opened, vented and ready for inspection by surveyors at the appropriate time. all pollution control requirements are met. crew persons are briefed on the changed workplace conditions & supplied with adequate P.P.E. Note the position of the fire hydrants ashore and the site of the dock supplied fire extinguishers. Keep a close watch on any hot work being done and stop any unsafe practices. Precautions on Relaunch Ensure that: all docking plugs have been replaced all intake gills/grates have been replaced all transducers are uncovered and wiped clean all tanks are boxed up (manhole/inspection covers are replaced) anchors are secured all loose gear is secured new paint is dry to manufacturer’s specifications shore power supply is disconnected there is sufficient water depth to relaunch sea cocks are open See Maintenance schedule See Spillage control plan

Approving officer Signed Date